## Slide 1
California Summit RF Environment
SOTA RF-source mapper · 605 summits mapped against 1.23 M FCC RF sources (ASR + ULS land-mobile/microwave + CDBS broadcast)
605
impacted summits
of 4,329 W6 summits
30%
MODERATE+ overload
184 summits at real risk
70 cm
most-threatened band
69 HIGH · 153 MOD+
96 MW
UHF-TV broadcast ERP
37× all other bands
Chart: Summits at HIGH overload risk, by ham band
| 70 cm | 23 cm | 2 m | 6 m
HIGH summits | 69 | 42 | 24 | 4
Key findings
Broadcast powers it, land-mobile blankets it
UHF-TV alone is 96 MW of ERP, but VHF/UHF/microwave land-mobile reach 330–399 summits each vs 121–131 for broadcast.
70 cm is squeezed from both sides
Full-power UHF-TV (470–700 MHz) above and UHF public-safety/GMRS (450–470) below — the worst band by far.
Distance-aware capture
A field-strength model (ERP/d²) pulls in far megawatt masts — e.g. Sutro Tower's ~7 MW, 1.9 km from Mt Davidson.
Notes: Summary of the SOTA RF-source mapper, W6 (California). 605 of 4,329 summits have an in-range fixed RF source; 184 (30%) show MODERATE-or-worse ham-band overload risk. 70 cm is the most-threatened amateur band. Data: FCC ASR structures + ULS land-mobile/microwave + CDBS broadcast = 1.23 M sources. Field-strength inclusion model captures distant high-ERP broadcast masts.